Report for : Mark Callictt / Sam Falkner

Compiled by : Mark Smith

| WELL | CBA F27 |
| --- | --- |
| DATE | 22-05-2009 |
| REPORT # | 16 |
| MIDNIGHT ACTIVITY | Drill ahead 9-7/8” production hole to TD. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3093.0 mMDRT |  | MINIMUM | 22.7 | 2827.0 |
| TVD | 2009.2 mTVDRT |  | MAXIMUM | 114.1 | 2748.0 |
| PROGRESS LAST 24 hrs | 817.0 m |  | AVERAGE | 67.5 | 2276.0-3093.0 |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance |  |  |  |  | 3449.6 | 2185.0 |
| Top of Latrobe Group |  |  |  |  | 3773.9 | 2352.0 |
| Top Coarse Clastics |  |  |  |  | 3777.8 | 2354.0 |
| Top M101B Upper Reservoir |  |  |  |  | 3779.7 | 2355.0 |
| Top M101D Upper Reservoir |  |  |  |  | 3787.5 | 2359.0 |
| Top M101D Lower Reservoir |  |  |  |  | 3797.2 | 2364.0 |
| Top M101E Reservoir |  |  |  |  | 3814.7 | 2373.0 |
| M111 Reservoir |  |  |  |  | 3838.0 | 2385.0 |
| M131 Reservoir |  |  |  |  | 3898.2 | 2416.0 |
| Original Oil Water Contact |  |  |  |  | 3942.8 | 2439.0 |
| Total Depth |  |  |  |  | 3982.8 | 2459.6 |

| Current Formation | LIMESTONE |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 2748.0 | 32.7 | 0.586 | 0.002 | - | - | - | 0 |
| MAX (GFF) | 2457.0 | 28.7 | 0.560 | 0.004 | 0.001 | - | - | 0 |
| BG (Reserval) | 2276.0-3093.0 | 22.0 | 0.399 | 0.002 | - | - | - | - |
| BG (GFF) | 2276.0-3093.0 | 22.0 | 0.411 | 0.003 | 0.001 | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 7 | 6 |
| SIZE (in) | 9-7/8 | 9-7/8 |
| MANUFACTURER/TYPE | Reed Hycalog / RSD616M | Mill Tooth |
| JETS (/32 inch) | 6 x 18 | 3 x 22 |
| DEPTH IN (m) | 603 | 599 |
| DEPTH OUT (m) | - | 603 |
| METRES ON RUN (m) | 2490.0 | 4 |
| HRS ON BTM 24hrs/total | 12.1 / 50.5 | 0.0 / 0.6 |
| BIT CONDITION | - | - |
| RPM RANGE 24hrs | 150-170 | - |
| Pump Hrs 24 hrs / total | 21.2 / 75.8 | 0 / 14.2 |
| Krevs 24 hrs / total | 110 / 440 | 0 / 2 |

| 24 HOUR SUMMARY | Drill ahead and survey 9-7/8” production hole as per Anadrill’s instructions from 2276.0 mMDRT to 2823.0 mMDRT. Circulate and work pipe from 2823.0 mMDRT to 2800.0 mMDRT due to Scomi mono pump blockage. Drill ahead and survey 9-7/8” production hole as per Anadrill’s instructions from 2823.0 mMDRT to 3093.0 mMDRT. |
| --- | --- |
| 23-05-2009 5AM UPDATE | Drill ahead and survey 9-7/8” production hole as per Anadrill’s instructions from 3093.0 mMDRT to 3268.0 mMDRT. 5AM DEPTH: 3268.0 mMDRT (2100.0 mTVDRT) |