Report for : Mark Calicutt / Sam Falkner

Compiled by : Mark Smith

| WELL | CBA F27 |
| --- | --- |
| DATE | 23-05-2009 |
| REPORT # | 17 |
| MIDNIGHT ACTIVITY | Drill ahead 9-7/8” production hole to TD. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3676.0 mMDRT |  | MINIMUM | 18.7 | 3117.0 |
| TVD | 2309.4 mTVDRT |  | MAXIMUM | 119.9 | 3533.0 |
| PROGRESS LAST 24 hrs | 583.0 m |  | AVERAGE | 58.9 | 3093.0-3676.0 |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance | 3436.0 | 2184.7 | -2143.7 | 0.3 H | 3449.6 | 2185.0 |
| Top of Latrobe Group | 3768.0 | 2355.5 | -2114.5 | 3.5L | 3773.9 | 2352.0 |
| Top Coarse Clastics |  |  |  |  | 3777.8 | 2354.0 |
| Top M101B Upper Reservoir |  |  |  |  | 3779.7 | 2355.0 |
| Top M101D Upper Reservoir |  |  |  |  | 3787.5 | 2359.0 |
| Top M101D Lower Reservoir |  |  |  |  | 3797.2 | 2364.0 |
| Top M101E Reservoir |  |  |  |  | 3814.7 | 2373.0 |
| M111 Reservoir |  |  |  |  | 3838.0 | 2385.0 |
| M131 Reservoir |  |  |  |  | 3898.2 | 2416.0 |
| Original Oil Water Contact |  |  |  |  | 3942.8 | 2439.0 |
| Total Depth |  |  |  |  | 3982.8 | 2459.6 |

| Current Formation | CALCAREOUS CLAYSTONE |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 3110.0 | 32.1 | 0.570 | 0.003 | - | - | - | 0 |
| MAX (GFF) | 3249.0 | 25 | 0.459 | 0.004 | 0.002 | - | - | 0 |
| BG (Reserval) | 3093.0-3676.0 | 14.5 | 0.253 | 0.001 | - | - | - | - |
| BG (GFF) | 3093.0-3676.0 | 12 | 0.213 | 0.003 | 0.001 | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 7 | 6 |
| SIZE (in) | 9-7/8 | 9-7/8 |
| MANUFACTURER/TYPE | Reed Hycalog / RSD616M | Mill Tooth |
| JETS (/32 inch) | 6 x 18 | 3 x 22 |
| DEPTH IN (m) | 603.0 | 599 |
| DEPTH OUT (m) | - | 603 |
| METRES ON RUN (m) | 3073.0 | 4 |
| HRS ON BTM 24hrs/total | 9.9 / 60.4 | 0.0 / 0.6 |
| BIT CONDITION | - | - |
| RPM RANGE 24hrs | 90-165 | - |
| Pump Hrs 24 hrs / total | 20.7 / 96.5 | 0 / 14.2 |
| Krevs 24 hrs / total | 82 / 522 | 0 / 2 |

| 24 HOUR SUMMARY | Drill ahead and survey 9-7/8” production hole as per Anadrill’s instructions from 3093.0 mMDRT to 3315.0 mMDRT. Circulate and work pipe from 3315.0 mMDRT to 3209.0 mMDRT due to Scomie mono pump blocked. Drill ahead and survey 9-7/8” production hole as per Anadrill’s instructions from 3315.0 mMDRT to 3332.0 mMDRT. Back ream out of hole from 3332.0 mMDRT to 3198.0 mMDRT due to Scomie mono pumped blocked up. At 3292.0 mMDRT conduct rig service, accumulator and BOP test. Run in hole from 3198.0 mMDRT to 3292.0 mMDRT and wash to bottom. Drill ahead and survey 9-7/8” production hole as per Anadrill’s instructions from 3332.0 mMDRT to 3676.0 mMDRT. |
| --- | --- |
| 24-05-2009 5AM UPDATE | Drill ahead and survey 9-7/8” production hole as per Anadrill’s instructions from 3676.0 mMDRT to 3801.0 mMDRT. 5AM DEPTH: 3801.0 mMDRT (2373.2 mTVDRT) |