Report for : Mark Calicutt  / Sam Falkner

Compiled by : Gareth Munro

| WELL | CBA F35 |
| --- | --- |
| DATE | 09-09-2009 |
| REPORT # | 12 |
| MIDNIGHT ACTIVITY | Drilling 9-7/8” Production hole. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 4065.0 mMDRT |  | MINIMUM | 39.05 | 3239.0 |
| TVD | 2249.51 mTVDRT |  | MAXIMUM | 110.46 | 3970.0 |
| PROGRESS LAST 24 hrs | 936 m |  | AVERAGE | 68.82 | - |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top of Lakes Entrance Formation |  |  |  |  | 3863.4 | 2165.0 |
| Top of Latrobe Group |  |  |  |  | 4251.8 | 2331.0 |
| TCC / M101B |  |  |  |  | 4254.2 | 2332.0 |
| M101D Upper |  |  |  |  | 4268.2 | 2338.0 |
| M101D Lower |  |  |  |  | 4277.6 | 2342.0 |
| M101E |  |  |  |  | 4296.3 | 2350.0 |
| 1AFS / M111 |  |  |  |  | 4312.7 | 2357.0 |
| B112 / M112 |  |  |  |  | 4375.8 | 2384.0 |
| 3AFS / M131 |  |  |  |  | 4380.5 | 2386.0 |
| B132 / M132 Upper |  |  |  |  | 4427.3 | 2406.0 |
| M132 Lower |  |  |  |  | 4436.7 | 2410.0 |
| 4AFS / M141 |  |  |  |  | 4464.7 | 2422.0 |
| B142 / M142 |  |  |  |  | 4488.2 | 2431.0 |
| OOWC |  |  |  |  | 4502.2 | 2438.0 |
| Total Depth |  |  |  |  | 4562.2 | 2463.0 |

| Current Formation | Lakes Entrance |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 3579.0 | 29.0 | 0.536 | 0.004 | 0.001 | 0.001 | 0.000 | - |
| MAX (GFF) | 3516.0 | 25.0 | 0.456 | 0.007 | 0.000 | 0.000 | 0.000 | - |
| BG (Reserval) | 3129 -4065 | 16.9 | 0.301 | 0.002 | 0.001 | 0.002 | 0.000 | 0 |
| BG (GFF) | 3129 -4065 | 13.2 | 0.240 | 0.002 | 0.000 | 0.000 | 0.000 | 0 |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 4 | 3RR |
| SIZE (in) | 9-5/8 | 14-3/4 |
| MANUFACTURER/TYPE | Reed Hycalog RSR616S-A1 | Reed Hycalog T11 |
| JETS (/32 inch) | 8 x 16 | 3 x 20, 1 x 18 |
| DEPTH IN (m) | 683.0 | 405.0 |
| DEPTH OUT (m) | - | 683.0 |
| METRES ON RUN (m) | 3382.0 | 278.0 |
| HRS ON BTM 24hrs/total | 13.6 / 51.5 | 9.4 |
| BIT CONDITION | - | 2-2-WT-A-E-E-E-IN-No-TD |
| RPM RANGE 24hrs | 132 – 166 |  |
| Pump Hrs 24 hrs / total | 20.5 / 82.1 | 18.3 |
| Krevs 24 hrs / total | 121.8 / 461.8 | 3.6 |

| 24 HOUR SUMMARY | Drill and survey 9-7/8” production hole from 3129.0 to 4050.0 mMDRT as per Anadrill’s instructions. Control drill and survey 9-7/8” production hole from 4050.0 to 4065.0 mMDRT at 50 m/hr max. |
| --- | --- |
| 10-09-2009 5 AM UPDATE | Control drill and survey 9-7/8” production hole from 4065.0 to 4089.0 mMDRT at 50 m/hr max. Circulate hole clean with 2 mud pumps whilst changing pop off on mud pump 3. Control drill and survey 9-7/8” production hole from 4089.0 to 4203.0 mMDRT at 50 m/hr max. 5AM DEPTH: 4203.0 mMDRT 2307.0 mTVDRT |