Report for : Mark Calicutt  / Sam Falkner

Compiled by : Gareth Munro

| WELL | CBA F35 |
| --- | --- |
| DATE | 10-09-2009 |
| REPORT # | 13 |
| MIDNIGHT ACTIVITY | Circulate hole clean at Total Depth. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 4573.0 mMDRT |  | MINIMUM | 6.42 | 4321.0 |
| TVD | 2464.83mTVDRT |  | MAXIMUM | 73.33 | 4179.5 |
| PROGRESS LAST 24 hrs | 508.0 m |  | AVERAGE | 39.07 | - |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top of Lakes Entrance Formation | 3867.1 | 2164.0 | -2123.0 | 1.0 H | 3863.4 | 2165.0 |
| Top of Latrobe Group | 4299.9 | 2348.0 | -2307.0 | 17.0 L | 4251.8 | 2331.0 |
| TCC / M101B | 4302.2 | 2349.0 | -2308.0 | 17.0 L | 4254.2 | 2332.0 |
| M101D Upper | - | - | - | - | 4268.2 | 2338.0 |
| M101D Lower | - | - | - | - | 4277.6 | 2342.0 |
| M101E | 4302.2 | 4349.0 | -2308.0 | 1.0 H | 4296.3 | 2350.0 |
| 1AFS / M111 | 4324.6 | 2358.5 | -2317.5 | 1.5 L | 4312.7 | 2357.0 |
| B112 / M112 | 4383.4 | 2383.5 | -2342.5 | 0.5 H | 4375.8 | 2384.0 |
| 3AFS / M131 | 4391.7 | 2387.0 | -2346.0 | 1.0 L | 4380.5 | 2386.0 |
| B132 / M132 Upper | 4437.8 | 2406.5 | -2365.5 | 0.5 L | 4427.3 | 2406.0 |
| M132 Lower | 4450.8 | 2412.0 | -2371.0 | 2.0 L | 4436.7 | 2410.0 |
| 4AFS / M141 | 4473.3 | 2421.5 | -2380.5 | 0.5 H | 4464.7 | 2422.0 |
| B142 / M142 | 4493.3 | 2430.0 | -2389.0 | 1.0 H | 4488.2 | 2431.0 |
| OOWC | 4512.2 | 2438.0 | -2397.0 | 0.0 | 4502.2 | 2438.0 |
| Total Depth | 4573.0 | 2463.83 | -2422.83 | 0.23 L | 4562.2 | 2463.6 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 4447.5 | 100.0 | 0.515 | 0.180 | 0.191 | 0.141 | 0.048 | - |
| MAX (GFF) | 4447.5 | 68.0 | 0.313 | 0.119 | 0.129 | 0.106 | 0.043 | - |
| BG (Reserval) | 4065.0 – 4573.0 | 21.1 | 0.150 | 0.031 | 0.030 | 0.024 | 0.008 | 0 |
| BG (GFF) | 4065.0 – 4573.0 | 18.1 | 0.117 | 0.027 | 0.026 | 0.024 | 0.011 | 0 |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 4 | 3RR |
| SIZE (in) | 9-5/8 | 14-3/4 |
| MANUFACTURER/TYPE | Reed Hycalog RSR616S-A1 | Reed Hycalog T11 |
| JETS (/32 inch) | 8 x 16 | 3 x 20, 1 x 18 |
| DEPTH IN (m) | 683.0 | 405.0 |
| DEPTH OUT (m) | 4573.0 | 683.0 |
| METRES ON RUN (m) | 3890.0 | 278.0 |
| HRS ON BTM 24hrs/total | 13.0 / 64.5 | 9.4 |
| BIT CONDITION | - | 2-2-WT-A-E-E-E-IN-No-TD |
| RPM RANGE 24hrs | 47 – 150 |  |
| Pump Hrs 24 hrs / total | 21.2 / 103.3 | 18.3 |
| Krevs 24 hrs / total | 81.8 / 543.6 | 3.6 |

| 24 HOUR SUMMARY | Control drill and survey 9-7/8” production hole from 4065.0 to 4089.0 mMDRT at 50 m/hr max. Circulate hole clean with 2 mud pumps whilst changing pop off on mud pump 3. Control drill and survey 9-7/8” production hole from 4089.0 to 4311.0 mMDRT at 50 m/hr max. Repair Scomi mud cleaner pump, circulate and work pipe from 4311.0 mMDRT to 4290.0 mMDRT whilst out of service. Control drill and survey 9-7/8” production hole from 4311.0 to 4398.0 mMDRT at 50 m/hr max. Crack found in box of drill pipe tool joint, lay out single and replace with new joint in string. Control drill and survey 9-7/8” production hole from 4398.0 to 4573.0 mMDRT at 50 m/hr max. |
| --- | --- |
| 11-09-2009 5 AM UPDATE | Circulate hole clean, 3 x bottoms up, rack one stand per bottoms up from 4573.0 mMDRT to 4466.0 mMDRT. Back ream out of hole from 4466.0 to 4343.0 mMDRT, ranging from 15 to 5 minutes per stand. 5AM DEPTH: 4573.00 mMDRT 2463.83 mTVDRT |