WEEKLY REPORT

Week Ending		2 August 2009

________________________________________________________________________________

Well			GV Moolort 3

Location		As drilled

7760599 m E	5889495 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		314.9 metres	Target depth

Well Details		0 – 4.5 m		Open Hole 	170mm

4.5 – 29.2 m		PQ Core

29.2 – 81.0 m		Open hole 	PCD

81.0 – 84.0 m		HQ Core

84.0 – 108.0 m	Open Hole	PCD

108.0 – 314.9 m	HQ Core

Casing			0 – 4.5 m 	PVC	150mm

0 – 18 m	PW

0 – 93 m	HW

0 – 314.9 m	Poly	63mm

Other	Vic DPI visited site 27 July 2009

________________________________________________________________________________

Well			GV Addington 1

Location		As drilled

735911 m E	5855955 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.6)

Well Depth		298.8 metres	completed

Well Details		0 – 4.8 m		Open Hole 	170mm

4.8 -128.8 m		PQ Core

128.8 – 137.2 m	HQ Core

137.2 – 170.7 m	Open hole PCD

170.7 – 298.8 m	HQ Core

Casing			0 – 4.8 m 	PVC	150mm

0 – 141 m	HW

0 – 298.8 m	Poly	63mm

Other	No issues

________________________________________________________________________________

Well			GV Stewart 1

Location		37.26 deg. S	143.91 deg E

757702 m E	5572312 m N	Zone 54(GDA 94)	approximate position

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		4.0 metres

Well Details		0 – 2 m	Open Hole 	170mm

2 – 4.0 m	PQ Core

Casing			0 – 2.0 m 	PVC	150mm

Other	No issues

________________________________________________________________________________

Safety	Core Shed

Geologist aggravated medial ligament injury, when picking up bag of cement. No medical treatment.

GV Addington 1

Drill offsider slipped and fell onto sand whilst working on core barrel. (core barrel on stand ~90cm above ground.). Incorrect core extraction technique. No medical treatment. Offsider remained at work.

Environment	No issues to report

Landholder Issues

No issues to report

Other		GV Moolort 3 completed drilling 31 July 2009

GV Addington 1 completed drilling 2 August 2009

GV Stewart 1 commenced drilling 2 August 2009

GV Goldsmith 1 expected to commence drilling 4 August 2009

Rob Murphy

Geogen Victoria

Ballarat Operations