WEEKLY REPORT

Week Ending		26 July 2009

________________________________________________________________________________

Well			GV Moolort 1

Location		As drilled

760595 m E	5889504 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		40.0 metres	Well abandoned

Well Details		0 – 10.0 m		Open Hole 	170mm

10.0 – 40.0 m		PQ Core

Casing			0 – 6.0 m 	PVC	150mm

0 – 15.0 m	PW

Other	PQ rods bogged in poorly consolidated sands in the Calivil Formation. Unable to retrieve rods from hole. Rods cut and 30 metres of rod string recovered. Six metres of PQ rod and PQ core barrel not recovered. Well abandoned.

________________________________________________________________________________

Well			GV Moolort 2

Location		As drilled

760597 m E	5889505 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		65.0 metres

Well Details		0 – 8.1 m		Open Hole 	170mm

8.1 – 26.2 m		PQ Core

26.2 – 65.0 m		Open hole	PCD

Casing			0 – 5.5 m 	PVC	150mm

0 – 9.0 m	PW

Other	At 65 metres the PCD sheared off and could not be recovered from well. Well abandoned.

________________________________________________________________________________

Well			GV Moolort 3

Location		As being drilled

7760599 m E	5889495 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		53.0 metres

Well Details		0 – 4.5 m		Open Hole 	170mm

4.5 – 29.2 m		PQ Core

29.2 – 53.0 m		Open hole 	PCD

Casing			0 – 4.5 m 	PVC	150mm

0 – 18 m	PW

Other	Access to paddock poor and internal paddock traffic being minimised

________________________________________________________________________________

Well			GV Addington 1

Location		37.41 deg. S	143.66 deg. E	(approx.)

735904 m E	5855956 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.6)

Well Depth		204.6 metres

Well Details		0 – 4.8 m		Open Hole 	170mm

4.8 -128.8 m		PQ Core

128.8 – 137.2 m	HQ Core

137.2 – 170.7 m	Open hole PCD

170.7 – 204.6 m	HQ Core

Casing			0 – 4.8 m 	PVC	150mm

0 – 141 m	HW

Other	Access to paddock being minimised

________________________________________________________________________________

Safety	GV Addington 1

Drill offsider tripped on well site bunding, whilst loading a HW rod onto rod truck and dropped the rod onto his leg. Minor bruising to leg. Offsider remained at work.

Environment	GV Carisbrook 2

During restoration of the well site a small hydraulic hose on the excavator blew. A small quantity of hydraulic fluid (<two litres) was spilt. Spill kit materials were immediately put in place. Next morning following repairs to the machine, all contaminated materials were removed from site.

Landholder Issues

GV Moolort 3

Paddock water supply line was punctured when erecting safety barrier fencing around the well site. Poly pipe was promptly repaired with minimal water loss

Other	GV Addington 1 expected to complete drilling 31 July 2009

GV Moolort 3 expected to complete drilling 31 July 2009

GV Goldsmith 1 expected to commence drilling 1 August 2009

GV Stewart 1 expected to commence drilling 1 August 2009

Rob Murphy

Geogen Victoria

Ballarat Operations