WEEKLY REPORT

Week Ending		30 August 2009

_______________________________________________________________________________

Well			GV Cameron 1A

Location		As drilled

748906 m E	5878549 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		214.6 metres		Well abandoned

Well Details		0 – 5.0 m		Open Hole 	170mm	GV Cameron 1

5.0 – 122.9 m		PQ Core			GV Cameron 1

122.9 – 204.0 m	HQ Core			GV Cameron 1

204.0 m				Wedge

204.2 – 214.6 m	HQ Core			GV Cameron 1A

Casing			0 – 2.0 m 	PVC	150mm

0 – 122.9 m	HW	cemented

Other	Approximately 210 metres of Poly casing was recovered from GV Cameron 1. During the attempted recovery process of the remaining 110 metres of Poly casing in GV Cameron 1 a wedge was commenced at 204 metres – GV Cameron 1A. At 214.6 metres the wedge collapsed. The drill string was recovered from the well and the recovery of the well, GV Cameron 1/1A was abandoned. The drill rig was moved approximately five metres on the site and GV Cameron 2 commenced

________________________________________________________________________________

Well			GV Cameron 2

Location		Approximate position

748905 m E	5878545 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		94.2 metres

Well Details		0 – 6.6 m		Open Hole 	170mm

6.6 – 52.2 m		PQ Core

52.2 – 92.1 m		Open Hole	PCD

92.1 – 94.2 m		PQ Core

Casing			0 – 6.6 m 	PVC	150mm

Other	No issues

________________________________________________________________________________

Safety	No incidents to report.

Environment	No issues to report

Landholder Issues

No issues to report

Other		GV Cameron 1/1A abandoned drilling 28 August 2009

GV Cameron 2 commenced drilling 28 August 2009

GV Leishman 2 commencement has been delayed, whilst GV Cameron 2 is drilled.

On 24 August, Officer of Vic DPI visited GV Addington 1 to observe logging truck and logging procedures and Core Shed facility at Yapeen.

Rob Murphy

Geogen Victoria

Ballarat Operations