WEEKLY REPORT

Week Ending		5 July 2009

________________________________________________________________________________

Well			GV Kooroocheang 1

Location		As Drilled

765397 m E	5869147 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.6)

Well Depth		320.0 metres	target depth

Well Details		0 – 12.0 m		Open Hole 	170mm

12.0 – 143.8 m	PQ Core

143.8 – 320.0 m	HQ Core

Casing			0 – 7.0 m 	PVC	150mm

0 – 143.0 m	HW	cemented

________________________________________________________________________________

Well			GV Leishman 1

Location		As Drilled

753307 m E	5872989 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		134.5 metres

Well Details		0 – 4.5 m		Open Hole 	170mm

4.5 – 120.2 m		PQ Core – high core losses

120.2 – 129.4 m	HW	Open hole

129.4 – 130.0 m	PCD 	Open hole

130.0 – 134.5 m	HQ Core – no core recovered

Casing			0 – 4.5 m 	PVC	150mm

0 -129.4 m	HW	All recovered

________________________________________________________________________________

Well			GV Cotswold 1

Location		37.16 deg S	143.87 deg N

754654 m E	5884060 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		263.0 metres

Well Details		0 – 21.0 m		Open Hole 	170mm

21.0 – 101.9 m	PQ Core

101.9 – 263.0 m	HQ Core

Casing			0 – 5.0 m 	PVC	150mm

0 – 102.0 m	HW	cemented

________________________________________________________________________________

Well			GV Werona 1

Location		37.25 deg S	144.03 deg N

237005 m E	5872719 m N	Zone 55	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.6)

Well Depth		63.4 metres

Well Details		0 – 10.9 m		Open Hole 	170mm

10.9 – 63.4 m		PQ Core

Casing			0 – 6.0 m 	PVC	150mm

0 -63.4 m	HW	cemented

________________________________________________________________________________

Safety	District hit by severe storm on 30 June 2009

Rig move between GV Leishman 1 and GV Cotswold 1 disrupted.

Empty tank and core trays blown off site into paddock at GV Leishman 1. All gear retrieved.

Rig shut down at GV Kooroocheang 1 during storm

Light vehicle hit by small tree branch on forestry road nearby to GV Cotswold 1. No damage.

Light vehicle near miss when tree branch fell in front of vehicle on highway in Yandoit area.

Environment	No issues to report

Landholder Issues

No issues

Other	GV Leishman stopped drilling 29 June 2009.

Unable to achieve target depth due to ground conditions.

GV Kooroocheang 1 completed drilling 30 June 2009

GV Cotswold 1 commenced drilling on 1 July 2009

GV Cotswold 1 expected to be completed 6 July 2009

GV Werona 1 commenced drilling on 2 July 2009

Rob Murphy

Geogen Victoria

Ballarat Operations