WEEKLY REPORT

Week Ending		9 August 2009

_______________________________________________________________________________

Well			GV Stewart 1

Location		As drilled

757727 m E	5872356 m N	Zone 54(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.13)

Well Depth		317.6 metres	target depth

Well Details		0 – 2.0 m		Open Hole 	170mm

2.0 – 110.9 m		PQ Core

110.9 – 317.6m	HQ Core

Casing			0 – 2.0 m 	PVC	150mm

0 – 110.9 m	HW	cemented

0 – 317.6 m	Poly	63mm

Other	No issues

________________________________________________________________________________

Well			GV Goldsmith 1

Location		39.55 deg. S	143.35 deg.E

707874 m E	5841116 m N	Zone 54	(GDA 94)

Drilling Contractor 	Titeline Pty Ltd, Ballarat (Rig No.6)

Well Depth		68.1 metres

Well Details		0 – 4.5 m		Open Hole 	170mm

4.5 – 68.1 m		PQ Core

Casing			0 – 4.5 m 	PVC	150mm

Other	No issues

________________________________________________________________________________

Safety	No incidents to report.

Environment	Site refurbishment of GV Moolort 1-3 and GV Addington 1 delayed due to unavailability of contractor

Landholder Issues

No issues to report

Other		GV Stewart 1 completed drilling 8 August 2009

GV Goldsmith 1 commenced drilling 4 August 2009

GV Cameron 1 expected to commence drilling 10 August 2009

Rob Murphy

Geogen Victoria

Ballarat Operations