| Date: | 17 Oct 2009 | Report Number: | 1 |
| --- | --- | --- | --- |
| Report Period: | 0000-2400 Hours | Last Casing Shoe: | N/A |
| Depth @ 2400hrs: | N/A mMDRT | Last Casing Size: | N/A |
| Previous 2400hr depth: | N/A mMDRT | Current Bit Size: | N/A |
| Progress: | 0 m | FIT: | N/A |
| Lag Depth: | N/A | Mud Weight: | N/A |
| Water Depth: | ~485 m LAT (TBC) | ECD: | N/A |
| RT: | 21.5 m (TBC) | Mud Type: | N/A |
| Last Survey Depth: | N/A | Mud Chlorides: | N/A |
| Deviation: | Inc / Azi | Est. Pore Press: | N/A |

## OPERATIONS SUMMARY

| 24 HOUR SUMMARY TO MIDNIGHT: | Completed rig tow from Westernport to Somerset-1 location. Deployed three anchors with Lewek Emerald support vessel. |
| --- | --- |
| NEXT 24 HOURS: | Complete deployment of the secondary anchors. Pretension the secondary anchors. Ballast down the rig. Conduct a shallow gas meeting. Make up the 914 mm (36”) and 444 mm (17.5”) BHAs. RIH with 914 mm BHA and TGB to spud in. |
| MIDNIGHT TO 0600hrs SUMMARY: | Completed deployment of primary anchors. Commenced deployment of the secondary anchors. |
| CURRENT OPERATION @ 06:00hrs: | Deploying secondary anchors with the Lewek Emerald support vessel. |

## GEOLOGICAL SUMMARY

LITHOLOGY

# No new formation drilled.

HYDROCARBON FLUORESCENCE

No new formation drilled.

# GAS SUMMARY

| Background | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| No drilling | - | - | - | - | - | - | - | - |
| Peaks | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | iC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |
| Connection | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |
| Trip | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |

FORMATION PRESSURE ESTIMATION

| ITEM | REMARKS |
| --- | --- |
| Mud weight | N/A |
| Connection gas | N/A |
| Trip gas | N/A |
| Background gas | N/A |
| Dxc exponent | N/A |
| ROP | N/A |
| Ditch cuttings | N/A |
| Mud temperature out | N/A |
| MWD resistivity | N/A |
| Pore Pressure Estimate | N/A |

# SAMPLE QUALITY

No drilling.

### MUDLOGGING EQUIPMENT/PERSONNEL

Personnel: 2 Data Engineers, 3 Mudloggers, 1 Trainee Mudlogger

Equipment: The 2 Wellsite Geologists have and will continue to check the BHI consumables for Somerset-1.  BHI will be monitoring depth using a Kelly bottle and have a back-up Kelly bottle. In the case of the back-up Kelly bottle failing a draw works depth encoder would be relied up for monitoring depth. BHI do not have a geolograph onboard. The only location for a geolograph is currently being used by SLB LWD.

### MWD/LWD

Personnel:  2 LWD Engineers

2 Directional Drillers

Equipment: Primary and back up tools for the 444 mm (17.5”) section are being checked and tested. Tools for the 311 mm (12.25”) section have not yet arrived on the rig.

###### WIRELINE

Personnel: No crew onboard.

### WELLSITE GEOLOGISTS

David Hartney / Todd Teasdale

| FIELD REPORTED PROVISIONAL FORMATION TOPS |
| --- |
| Formation | Marker | Predicted Top (m) | Actual Top (m) | Diff. | Reason |
|  |  | MDRT | TVDSS | +/- | MDRT | TVDRT | TVDSS | (MD) |  |
| Seabed |  | 506.5 | 485 | 15 |  |  |  |  |  |
| Port Campbell Limestone |  | 731.5 | 710 | 30 |  |  |  |  |  |
| Gellibrand Marl |  | 1022.5 | 1001 | 30 |  |  |  |  |  |
| Base Miocene Marker |  | 1313.5 | 1292 | 40 |  |  |  |  |  |
| Narrawaturk Marl |  | 1585.5 | 1564 | 70 |  |  |  |  |  |
| Dilwyn Formation |  | 1640.5 | 1619 | 70 |  |  |  |  |  |
| Massacre Formation |  | 1690.5 | 1669 | 70 |  |  |  |  |  |
| Skull Creek Formation |  | 2087.5 | 2066 | 90 |  |  |  |  |  |
| Thylacine Member |  | 2814.5 | 2793 | 170 |  |  |  |  |  |
| Flaxman Formation |  | 2840.5 | 2819 | 180 |  |  |  |  |  |
| Waare Formation |  | 3136.5 | 3115 | 220 |  |  |  |  |  |
| Eumeralla Formation |  | 3258.5 | 3237 | 240 |  |  |  |  |  |
| TD |  | 3308 | 3287 | 240 |  |  |  |  |  |

Note: All depths LAT

CUTTINGS SAMPLING SUMMARY (24 hr period)

| Depth Interval (mMDRT) | Sampling rate | Samples missed |
| --- | --- | --- |
| No drilling |  |  |

MUD / MUD FILTRATE SAMPLES (24 hr period)

| Depth (mMDRT) | Sample type |
| --- | --- |
| No drilling |  |

ISOTUBE SAMPLES (24 hr period)

| Depth (mMDRT) | Date | Time | TG% | Remarks |
| --- | --- | --- | --- | --- |
| No drilling |  |  |  |  |

# DEPTH TABLE (add rows as required)

|  | mMDRT unless otherwise stated | Precision of depth quoted | Remark |
| --- | --- | --- | --- |
| RTE |  | 1dp |  |
| Mudline |  | 1dp |  |
| Water Depth |  | 1dp |  |
| 914 mm (36”) TD |  | 0dp |  |
| 508 mm (20”) csg shoe |  | 0dp |  |
| 445mm (17-1/2”) TD |  | 0dp |  |
| 340mm (13-3/8”) csg shoe |  | 0dp |  |
| 311mm (12-1/4”) TD |  | 0dp |  |