| Date: | 23 Oct 2009 | Report Number: | 7 |
| --- | --- | --- | --- |
| Report Period: | 0000-2400 Hours | Last Casing Shoe: | 1278.6 mMDRT |
| Depth @ 2400hrs: | 1284 mMDRT | Last Casing Size: | 340 mm (13-3/8”) |
| Previous 2400hr depth: | 1284 mMDRT | Current Bit Size: | N/A |
| Progress: | 0 m | FIT: | N/A |
| Lag Depth: | N/A | Mud Weight: | 1.25 sg |
| Water Depth: | 503.0 m LAT | ECD: | N/A |
| RT: | 21.5 m | Mud Type: | Ultradrill |
| Last Survey Depth: | 1251.88 mMDRT | Mud Chlorides: | 72,000 |
| Deviation: | Inc 0.96° Azi 60.07° | Est. Pore Press: | 1.03 sg EMW |

## OPERATIONS SUMMARY

| 24 HOUR SUMMARY TO MIDNIGHT: | Continued to run BOP on riser. Attached choke and kill lines. Kedged BOP over well head. Landed BOP and pressure tested the choke and kill lines. Installed slip joint and diverter. Laid out BOP/riser handling equipment. Tested shear rams and BOP connector. Commenced picking up and making up 127 mm (5”) drill pipe singles. |
| --- | --- |
| NEXT 24 HOURS: | Complete picking up drill pipe. Lay out 444 mm (17 1/2”) BHA. Pick up and make up 311 mm (12 1/4”) BHA. Complete rig service prior to running in hole and tagging top of cement. Drill out shoe track whilst displacing to new Ultradrill mud system. Drill 3 m of new formation. Conduct LOT and perform SCR and CLR tests. Drill ahead 311 mm (12 1/4”) hole section. |
| MIDNIGHT TO 0600hrs SUMMARY: | Picked up and made up 127 mm (5”) drill pipe singles. Function tested the BOPs and commenced installing the diverter insert packer and tested diverter same. |
| CURRENT OPERATION @ 06:00hrs: | Laying out 444 mm (17 1/2”) BHA. |

## GEOLOGICAL SUMMARY

LITHOLOGY

# No new formation drilled.

HYDROCARBON FLUORESCENCE

# No new formation drilled.

# GAS SUMMARY

| Background | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| No returns | - | - | - | - | - | - | - | - |
| Peaks | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | iC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |
| Connection | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |
| Trip | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |

FORMATION PRESSURE ESTIMATION

| ITEM | REMARKS |
| --- | --- |
| Mud weight | 1.25 sg |
| Connection gas | N/A |
| Trip gas | N/A |
| Background gas | N/A |
| Dxc exponent | Minor cutback at 1104 mMDRT. No other cut backs observed. |
| ROP | Normal reflecting changes in formation |
| Ditch cuttings | N/A |
| Mud temperature out | N/A |
| MWD resistivity | N/A |
| Pore Pressure Estimate | 1.03 sg EMW (estimate from town) |

# SAMPLE QUALITY

# No new formation drilled.

### MUDLOGGING EQUIPMENT/PERSONNEL

Personnel: 2x Data Engineers, 4x Mudloggers (sharing sample catching duties).

Equipment: All consumables checked and sufficient to complete the well.  Chromatograph fully calibrated.

### MWD/LWD

Personnel:  3x LWD Engineers

2x Directional Drillers

Equipment: All primary and back-up 311 mm (12-1/4”) LWD tools have been checked – OK.  It is planned to lay down the 444 mm (17.5”) tools in the next 24 hours in readiness for back load.

###### WIRELINE

Personnel: No crew onboard.

REMARKS

None

### WELLSITE GEOLOGISTS

David Hartney / Todd Teasdale

| FIELD REPORTED PROVISIONAL FORMATION TOPS |
| --- |
| Formation | Marker | Predicted Top (m) | Actual Top (m) | Diff. | Reason |
|  |  | MDRT | TVDSS | +/- | MDRT | TVDRT | TVDSS | (MD) |  |
| Seabed |  | 506.5 | 485 | 15 | 524.5 | 524.5 | 503.0 | +18 | Incorrect velocity in seismic model (+18m applied) |
| Port Campbell Limestone |  | 749.5 | 728.0 | 30 |  |  |  |  |  |
| Gellibrand Marl |  | 1040.5 | 1019.0 | 30 | 1060 | 1059.95 | 1038.45 | +19.45 | Decrease in ROP |
| Base Miocene Marker |  | 1331.5 | 1310.0 | 40 |  |  |  |  |  |
| Narrawaturk Marl |  | 1603.5 | 1582.0 | 70 |  |  |  |  |  |
| Dilwyn Formation |  | 1658.5 | 1637.0 | 70 |  |  |  |  |  |
| Massacre Formation |  | 1708.5 | 1687.0 | 70 |  |  |  |  |  |
| Skull Creek Formation |  | 2105.5 | 2084.0 | 90 |  |  |  |  |  |
| Thylacine Member |  | 2832.5 | 2811.0 | 170 |  |  |  |  |  |
| Flaxman Formation |  | 2858.5 | 2837.0 | 180 |  |  |  |  |  |
| Waare Formation |  | 3154.5 | 3133.0 | 220 |  |  |  |  |  |
| Eumeralla Formation |  | 3276.5 | 3255.0 | 240 |  |  |  |  |  |
| TD |  | 3326.0 | 3304.4 | 240 |  |  |  |  |  |
| TD max |  | 3566.0 | 3544.5 |  |  |  |  |  |  |

Note: All depths LAT

# DEPTH TABLE

|  | mMDRT unless otherwise stated | Precision of depth quoted | Remark |
| --- | --- | --- | --- |
| RTE | 21.5 above LAT | 1dp |  |
| Mudline | 524.5 | 1dp |  |
| Water Depth | 524.5 | 1dp |  |
| 914 mm (36”) TD | 572.5 | 1dp |  |
| 508 mm (20”) csg shoe | 569.44 | 2dp | Tagged TOC @ 567.25 |
| 445mm (17-1/2”) TD | 1284.0 | 1dp |  |
| 340mm (13-3/8”) csg shoe | 1278.6 | 1dp |  |
| 311mm (12-1/4”) TD |  | 0dp |  |

CUTTINGS SAMPLING SUMMARY

| Depth Interval (mMDRT) | Sampling rate | Samples missed |
| --- | --- | --- |
| No returns |  |  |

MUD / MUD FILTRATE SAMPLES

| Depth (mMDRT) | Sample type |
| --- | --- |
| None |  |

ISOTUBE SAMPLES

| Depth (mMDRT) | Date | Time | TG% | Remarks |
| --- | --- | --- | --- | --- |
| None |  |  |  |  |