| Date: | 24 Oct 2009 | Report Number: | 8 |
| --- | --- | --- | --- |
| Report Period: | 0000-2400 Hours | Last Casing Shoe: | 1278.6 mMDRT |
| Depth @ 2400hrs: | 1284 mMDRT | Last Casing Size: | 340 mm (13-3/8”) |
| Previous 2400hr depth: | 1284 mMDRT | Current Bit Size: | 311 mm (12-1/2”) |
| Progress: | 0 m | FIT: | N/A |
| Lag Depth: | N/A | Mud Weight: | 1.25 sg |
| Water Depth: | 503.0 m LAT | ECD: | 1.28 sg EMW |
| RT: | 21.5 m | Mud Type: | Ultradrill |
| Last Survey Depth: | 1251.88 mMDRT | Mud Chlorides: | 70,000 |
| Deviation: | Inc 0.96° Azi 60.07° | Est. Pore Press: | 1.03 sg EMW |

## OPERATIONS SUMMARY

| 24 HOUR SUMMARY TO MIDNIGHT: | Picked up and made up 127 mm (5”) drill pipe. Function tested BOPs and installed diverter insert packer and tested. Laid out 444 mm (17-1/2”) BHA. Performed rig service. Picked up and made up 311mm (12-1/4”) BHA. RIH and shallow tested tools – sonic tool failed. Sonic and ADN tools were replaced with back up tools. RIH to 1235 mMDRT, picking up drill pipe from the deck. |
| --- | --- |
| NEXT 24 HOURS: | Continue to RIH, tag top of cement, drill out shoe track whilst displacing to new Ultradrill mud system. Drill 5 m of new formation. Conduct LOT and perform SCR and CLR tests. Drill ahead in 311 mm (12-1/4”) hole section. |
| MIDNIGHT TO 0600hrs SUMMARY: | Continued RIH. Tagged top of cement at 1244.87 mMDRT. Displaced to Ultradrill mud system whilst drilling cement shoe track. |
| CURRENT OPERATION @ 06:00hrs: | Drilling shoetrack at 1254 mMDRT. |

## GEOLOGICAL SUMMARY

LITHOLOGY

# No new formation drilled.

HYDROCARBON FLUORESCENCE

# No new formation drilled.

# GAS SUMMARY

| Background | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| No returns | - | - | - | - | - | - | - | - |
| Peaks | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | iC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |
| Connection | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |
| Trip | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | IC5 (%) | NC5 (%) |
| N/A | - | - | - | - | - | - | - | - |

FORMATION PRESSURE ESTIMATION

| ITEM | REMARKS |
| --- | --- |
| Mud weight | 1.25 sg |
| Connection gas | N/A |
| Trip gas | N/A |
| Background gas | N/A |
| Dxc exponent | Minor cutback at 1104 mMDRT. No other cut backs observed. |
| ROP | Normal reflecting changes in formation |
| Ditch cuttings | N/A |
| Mud temperature out | N/A |
| MWD resistivity | N/A |
| Pore Pressure Estimate | 1.03 sg EMW (estimate from town) |

# SAMPLE QUALITY

# No new formation drilled.

### MUDLOGGING EQUIPMENT/PERSONNEL

Personnel: 2x Data Engineers, 4x Mudloggers (sharing sample catching duties).

Equipment: All consumables checked and sufficient to complete the well.  Chromatograph, total gas detection system and CO2 sensor have been calibrated.

### MWD/LWD

Personnel:  3x LWD Engineers

2x Directional Drillers

Equipment: During the first shallow hole test RT communication to the sADN tool failed. The tool was broken out and laid down while checks were done on the sonic tool. After inspection the sonic was found to have a faulty extender. The sonic was laid out. The back-up sonic and sADN tools were picked up.

The 444 mm (17.5”) tools are due to be back loaded on 25th October 2009.

| Sensor | Distance from Bit (m) |
| --- | --- |
| Pressure (Arc) | 9.31 |
| Resistivity(Arc) | 10.03 |
| Gamma Ray (Arc) | 10.08 |
| Vibration (TeleScope) | 17.05 |
| Direction & Inclination (TeleScope) | 18.05 |
| Delta T (sonic) | 27.56 |
| Ultrasonic (sADN) | 33.34 |
| Density (sADN) | 33.51 |
| Neutron (sADN) | 35.49 |

###### WIRELINE

Personnel: No crew onboard.

REMARKS

None

### WELLSITE GEOLOGISTS

David Hartney / Todd Teasdale

| FIELD REPORTED PROVISIONAL FORMATION TOPS |
| --- |
| Formation | Marker | Predicted Top (m) | Actual Top (m) | Diff. | Reason |
|  |  | MDRT | TVDSS | +/- | MDRT | TVDRT | TVDSS | (MD) |  |
| Seabed |  | 506.5 | 485 | 15 | 524.5 | 524.5 | 503.0 | +18 | Incorrect velocity in seismic model (+18m applied) |
| Port Campbell Limestone |  | 749.5 | 728.0 | 30 |  |  |  |  |  |
| Gellibrand Marl |  | 1040.5 | 1019.0 | 30 | 1060 | 1059.95 | 1038.45 | +19.45 | Decrease in ROP |
| Base Miocene Marker |  | 1331.5 | 1310.0 | 40 |  |  |  |  |  |
| Narrawaturk Marl |  | 1603.5 | 1582.0 | 70 |  |  |  |  |  |
| Dilwyn Formation |  | 1658.5 | 1637.0 | 70 |  |  |  |  |  |
| Massacre Formation |  | 1708.5 | 1687.0 | 70 |  |  |  |  |  |
| Skull Creek Formation |  | 2105.5 | 2084.0 | 90 |  |  |  |  |  |
| Thylacine Member |  | 2832.5 | 2811.0 | 170 |  |  |  |  |  |
| Flaxman Formation |  | 2858.5 | 2837.0 | 180 |  |  |  |  |  |
| Waare Formation |  | 3154.5 | 3133.0 | 220 |  |  |  |  |  |
| Eumeralla Formation |  | 3276.5 | 3255.0 | 240 |  |  |  |  |  |
| TD |  | 3326.0 | 3304.4 | 240 |  |  |  |  |  |
| TD max |  | 3566.0 | 3544.5 |  |  |  |  |  |  |

Note: All depths LAT

# DEPTH TABLE

|  | mMDRT unless otherwise stated | Precision of depth quoted | Remark |
| --- | --- | --- | --- |
| RTE | 21.5 above LAT | 1dp |  |
| Mudline | 524.5 | 1dp |  |
| Water Depth | 524.5 | 1dp |  |
| 914 mm (36”) TD | 572.5 | 1dp |  |
| 508 mm (20”) csg shoe | 569.44 | 2dp | Tagged TOC @ 567.25 |
| 445mm (17-1/2”) TD | 1284.0 | 1dp |  |
| 340mm (13-3/8”) csg shoe | 1278.6 | 1dp |  |
| 311mm (12-1/4”) TD |  | 0dp |  |

CUTTINGS SAMPLING SUMMARY

| Depth Interval (mMDRT) | Sampling rate | Samples missed |
| --- | --- | --- |
| No returns |  |  |

MUD / MUD FILTRATE SAMPLES

| Depth (mMDRT) | Sample type |
| --- | --- |
| None |  |

ISOTUBE SAMPLES

| Depth (mMDRT) | Date | Time | TG% | Remarks |
| --- | --- | --- | --- | --- |
| None |  |  |  |  |