Report for : Greg Doty / Sam Falkner

Compiled by : Gareth Munro / Phil Rady

| WELL | WKF W8A |
| --- | --- |
| DATE | 8-12-2009 |
| REPORT # | 10 |
| MIDNIGHT ACTIVITY | Pump out of hole. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 4535.00 m |  | MINIMUM | 12.99 | 4533.5 |
| TVD | 2455.57 m |  | MAXIMUM | 91.93 | 4439.5 |
| PROGRESS LAST 24 hrs | 184.0 |  | AVERAGE | 37.55 |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base of High Velocity Channel | 2304.0 | 1378.4 | -1336.73 | -3.3H | 2310.0 | 1381.7 |
| Mid Miocene Marker | 3838.0 | 1843.9 | -1802.16 | 2.2L | 3840.0 | 1841.7 |
| Top of Lakes Entrance Formation | 3973.0 | 1933.6 | -1891.9 | -8.1H | 3940.0 | 1941.7 |
| Top of Latrobe Group | 4352.5 | 2274.2 | -2232.5 | 3.1L | 4352.0 | 2271.1 |
| Top P1.1 West | 4382.0 | 2303.7 | -2262.0 | 7.0L | 4378.0 | 2297.7 |
| Top Coarse Clastics (SBP3) | 4397.0 | 2318.7 | -2277.0 | 7.0L | 4392.0 | 2311.7 |
| Top M1.3U (PSB7) | 4416.0 | 2337.7 | -2296.0 | 2.0L | 4416.0 | 2335.7 |
| PSB5 | 4422.0 | 2343.7 | -2302.0 | 2.0L | 4422.0 | 2341.7 |
| PSB4 | 4427.0 | 2348.7 | -2307.0 | 3.0L | 4426.0 | 2345.7 |
| Top M1.4U (SB13) | 4435.0 | 2356.7 | -2315.0 | 2.0L | 4435.0 | 2354.7 |
| Top M1.4L | 4451.0 | 2372.7 | -2331.0 | 1.0L | 4452.0 | 2371.7 |
| M1.4C | 4458.0 | 2379.7 | -2338.0 | 2.0L | 4458.0 | 2377.7 |
| M1.4C OOWC | 4459.0 | 2380.7 | -2339.0 | 1.2L | 4459.0 | 2379.5 |
| Top M1.5 | 4466.0 | 2387.7 | -2346.0 | 0.0 | 4468.0 | 2387.7 |
| M1.4B OOWC | 4472.0 | 2393.7 | -2352.0 | 5.3L | 4469.0 | 2388.4 |
| Total Depth | 4535.0 | 2455.57 | -2413.87 | 7.27L | 4529.0 | 2448.3 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 4397.0 | 80.0 | 0.568 | 0.140 | 0.151 | 0.097 | 0.029 | - |
| MAX (GFF) | 4447.5 | 83.0 | 1.023 | 0.107 | 0.093 | 0.060 | 0.023 | - |
| BG (Reserval) | 4351.0 – 4535.0 | 32.2 | 0.244 | 0.049 | 0.054 | 0.038 | 0.012 | 0 |
| BG (GFF) | 4351.0 – 4535.0 | 36.8 | 0.399 | 0.042 | 0.041 | 0.032 | 0.013 | 0 |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 1 |  |
| SIZE (in) | 9-7/8 |  |
| MANUFACTURER/TYPE | Reed Hycalog RSR616S-A1 |  |
| JETS (/32 inch) | 8 x 16 |  |
| DEPTH IN (m) | 830.0 |  |
| DEPTH OUT (m) | 4535.0 |  |
| METRES ON RUN (m) | 3705.0 |  |
| HRS ON BTM 24hrs/total | 4.9 / 48.6 |  |
| BIT CONDITION |  |  |
| RPM RANGE 24hrs | 90 - 159 |  |
| Pump Hrs 24 hrs / total | 16.9 / 104.6 |  |
| Krevs 24 hrs / total | 2.2 / 418.2 |  |

| 24 HOUR SUMMARY | Continue to drill ahead 9-7/8” production hole from 4351.0 m to 4535.0 mMDRT Total Depth as per Anadrill’s instructions. Take survey and conduct slow circulation rates and flow check well. Circulate and rotate whilst Anadrill down link tools. Commence to clean hole by circulating 3 bottoms up whilst racking back 1 stand per bottoms up. Pump and back ream out of hole to 4390.0 mMDRT spot 50 bbls of LCM pill at 4390.0 mMDRT. Continue to pump and back ream out of hole. |
| --- | --- |
| 09-12-2009 5 AM UPDATE | Continue to pump and back ream out of hole to 2379.0 mMDRT. 4535.0 mMDRT (2455.57 mTVDRT) |