LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 45 | DFS: | 45 | DATE : | 30-11-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2,500 | LAST DEPTH : | 2,500 | 24 HR PROGRESS: |  | PTD : | 2466mj |
| TOTAL FUEL : | 4.200 | FUEL USAGE : | 1,000 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Schlumberger running VSP logs |
| Next 24 Hrs Op | Run alternate CBL tool - Pressure test Tubing spool-against Adaptor head and Hanger |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES @ 22.30 |
| --- | --- | --- | --- | --- |
| j Bit Number |  |  |  | Drilling |  |  | Density |  | S.G. |
| Size (mm) |  |  |  | Tripping |  |  | Viscosity |  | Sec |
| Make |  |  |  | Standy |  |  | Water Loss |  | Cc |
| Type |  |  |  | Wireline logging | 9.00 |  | pH |  | Strip |
| IADC Code |  |  |  | Testing/tools |  |  | Filter Cake |  | 32 nd |
| Serial Number |  |  |  | Circulate Sample |  |  | PV / YP |  | Cp/lb/100’ |
| Nozzles (32) |  |  |  | Casing |  |  | Gels |  | S/m |
| Depth in (m) |  |  |  | Cementing |  |  | Sand |  | % Vol |
| Depth out (m) |  |  |  | Drill stem testing |  |  | Solids |  | % Vol |
| Total Metres |  |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours |  |  |  | Rig Service/slip & cut |  |  | K+ |  | Mg/l |
| WOB (kg) |  |  |  | Rig up/ d own bop | 10.00 |  | Chlorides |  | Mg/l |
| RPM |  |  |  | Drill out Cmt |  |  | K+ |  |  |
| Condition |  |  |  | Reaming |  |  | KCL | Stock | % |
| Impact Force |  |  |  | Wait On Cement | 5.00 |  | Daily Cost $ | Value on hand $35,645 |
| Jet Velocity |  |  |  | Test BOPs |  |  | Cum Cost $ | $94,369 |
| B.H.A.: |  |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  |  | ° at |  | m |  | Type | Amount |
| 0000 |  | Rigged down Halliburton from Rig floor |  |  | ° at |  | m |  | AMC Pac L |  |
|  |  | Rigged down Weatherford Casing tong |  |  | ° at |  | m |  | AMC Pac R |  |
|  |  | Secured Casing hanger with lockdown studs |  |  | ° at |  | m |  | Caustic |  |
|  |  | Laid out the landing joint |  |  | ° at |  | m |  | Xan Bore |  |
|  | 05.00 | Laid out Kelly and Mousehole-Kelly spinner |  |  | ° at |  | m |  | Bayrtes |  |
| 05.00 | 12.00 | Rigged down and removed all BOP equipment |  |  | ° at |  | m |  | Potassium Chloride |  |
| 12.00 | 15.00 | Installed Tubing Head adaptor and 10K Tree |  |  | ° at |  | m |  | AMC Biocide G |  |
| 15.00 |  | Rigged up Schlumberger for CBL run , had to flush |  |  |  |  |
|  | 17.00 | out excess grease from inside the Tree |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
| 17.00 | 24.00 | CBL Run |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure |  | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP |  | f/min |  | A.V. DP |  | Ft/min |
|  |  |  |  | A.V. DC |  | f/min |  | A.V. DC |  | Ft//mn |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | GPM |  |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 4½" | inch |
|  |  | Hunt 16 camp 4 Schlumberger 3 |  | Class Bulk |  |  | Weight | 41x15.1-169x13.5 | ppf |
|  |  | Lakes 2 |  | % |  |  |  | Grade | P110 |  |
|  |  | Mud logger 2 |  | % |  |  |  | Connection | BTC |  |
|  |  |  |  | % |  |  |  | Joints | 210 |  |
|  |  | RMN 1 left site today |  | % |  |  |  | Length | 2474.32 | m |
| Days since | LTA | 471 |  | Av. Wt |  |  | Shoe | 2478.72 | m |

,66