LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 23 | DFS: | 23 | DATE : | 8-11-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2,400 | LAST DEPTH : | 2,278 | 24 HR PROGRESS: | 122 | PTD : |  |
| TOTAL FUEL : | 4,100 | FUEL USAGE : | 2,400 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Drilled 156mm hole from 2,400 m to 2,403m with PDC Bit- Trip out for BHA change |
| Next 24 Hrs Op | Trip out for Drill assembly change-R.I.H with156mm drilling assembly –Drill ahead |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 5 Re-Run#4 |  |  | Drilling | 23.5 |  | Density | 1.152 | S.G. |
| Size (mm) | 156 |  |  | Tripping |  |  | Viscosity | 36 | Sec |
| Make | Smith |  |  | Surveys |  |  | Water Loss | 22.8 | Cc |
| Type | MDi613 |  |  | Wireline logging |  |  | pH | 8.0 | Strip |
| IADC Code |  |  |  | Testing/tools |  |  | Filter Cake | 2 | 32 nd |
| Serial Number | JD1042 |  |  | Circulate Sample |  |  | PV / YP | 8/17 | Cp/lb/100’ |
| Nozzles (32) | 3 x 12 |  |  | Casing |  |  | Gels | 4 / 7 | S/m |
| Depth in (m) | 1378 / 1478 |  |  | Cementing |  |  | Sand | 0.40 | % Vol |
| Depth out (m) | 1478 / SIH |  |  | Surveys |  |  | Solids | 7.3 | % Vol |
| Total Metres | 100 / 922 |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours | 7.5 / 114.5 |  |  | Rig Service/slip & cut | 0.5 |  | K+ | 5,250 | Mg/l |
| WOB (kg) | 2,000/5000 |  |  | Rig up/ d own bop |  |  | Chlorides | 6,200 | Mg/l |
| RPM | 90 /100 |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition |  |  |  | Reaming |  |  | KCL | 1.0 | % |
| Impact Force | 237 |  |  | Wait On Cement |  |  | Daily Cost $ |  |
| Jet Velocity | 215 |  |  | Test BOPs |  |  | Cum Cost $ | 62,297 |
| B.H.A.: 5 | 156mm Bit-NBS-NMDC-Stab-2 x DC-STB-12 x DC-Jars-2 xDC |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 1½º N60E | ° at | 1354 | m |  | Type | Amount |
| 0000 | 12.00 | Drilled 156mm hole from 2,278m to 2,345m |  | 4ºN340W | ° at | 1768 | m |  | AMC Pac L |  |
| 12.00 | 12.30 | Serviced the rig |  | 12ºN340W | ° at | 2093 | m |  | AMC Pac R |  |
| 12.30 | 24.00 | Drilled 156mm hole from 2,345m to 2,400m |  | 18.5 | ° at | 2235 | m |  | Lakes Pac R |  |
|  |  |  |  | N340W | ° at |  | m |  | Xan Bore |  |
|  |  |  |  |  | ° at |  | m |  |  |  |
|  |  |  |  |  | ° at |  | m |  |  |  |
|  |  |  |  |  | ° at |  | m |  |  |  |
|  |  |  |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
|  |  | String pick up 115k |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  | Down 105k |  | Pressure | 10,600 | kPa |  | Pressure |  | KPa |
|  |  | Held BOP Drill |  | A.V. DP | 223 | f/min |  | A.V. DP |  | Ft/min |
|  |  |  |  | A.V. DC | 394 | f/min |  | A.V. DC |  | Ft//mn |
|  |  |  |  | SPM | 40 |  | SPM |  |
|  |  |  |  | GPM | 240 |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 7" | inch |
|  |  | Hunt 17 Camp 4 |  | Class Bulk |  |  | Weight | 26 | ppf |
|  |  | Lakes 4 |  | % |  |  |  | Grade | K-55 |  |
|  |  | Mud logger 2 |  | % |  |  |  | Connection | BTC |  |
|  |  | Farley Riggs 4 |  | % |  |  |  | Joints | 117 |  |
|  |  | RMN 1 |  | % |  |  |  | Length | RT-Brd Hd 5.0 | m |
| Days since | LTA |  |  | Av. Wt |  |  | Shoe | 1376m from RKB | m |

,66