LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 24 | DFS: | 24 | DATE : | 9-11-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2,413 | LAST DEPTH : | 2,400 | 24 HR PROGRESS: | 13 | PTD : |  |
| TOTAL FUEL : | 1,700 | FUEL USAGE : | 2,400 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Drilled 156mm hole from 2,413 m to 2,432m Average ROP 12.5hrs = 2.32mph |
| Next 24 Hrs Op | Drill ahead |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 5 Re-Run#4 | 6 New |  | Drilling | 7.5 |  | Density | 1.158 | S.G. |
| Size (mm) | 156 | 156 |  | Tripping | 13.0 |  | Viscosity | 37 | Sec |
| Make | Smith | Reed |  | Surveys |  |  | Water Loss | 20.1 | Cc |
| Type | MDi613 | R22AP |  | Wireline logging |  |  | pH | 8.0 | Strip |
| IADC Code |  | 5-1-7 |  | Testing/tools |  |  | Filter Cake | 2 | 32 nd |
| Serial Number | JD1042 | KD1019 |  | Circulate Sample |  |  | PV / YP | 11/9 | Cp/lb/100’ |
| Nozzles (32) | 3 x 12 | 3 x 14 |  | Casing |  |  | Gels | 2 / 5 | S/m |
| Depth in (m) | 1378 / 1478 | 2403 |  | Cementing |  |  | Sand | 0.40 | % Vol |
| Depth out (m) | / 2403 |  |  | Surveys |  |  | Solids | 7.4 | % Vol |
| Total Metres | 1025 |  |  | Circulate & Condition | 1.5 |  | Oil |  | % Vol |
| Hours | 123 |  |  | Rig Service/slip & cut | 1.5 |  | K+ | 11,500 | Mg/l |
| WOB (kg) | 2,000/5000 |  |  | Rig up/ d own bop |  |  | Chlorides | 20,000 | Mg/l |
| RPM | 90 /100 |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition | Cutters good / Erosion |  |  | Reaming | 0.5 |  | KCL | 2.2 | % |
| Impact Force | 237 |  |  | Wait On Cement |  |  | Daily Cost $ | 4,283 |
| Jet Velocity | 215 |  |  | Test BOPs |  |  | Cum Cost $ | 66,580 |
| B.H.A.: 5 | 156mm Bit-NBS-NMDC-1 x DC-STB-13 x DC-Jars-2 xDC |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 1½º N60E | ° at | 1354 | m |  | Type | Amount |
| 0000 | 01.00 | Drilled 156mm hole from 2,400m to 2,403m |  | 4ºN340W | ° at | 1768 | m |  | AMC Pac L | 4 |
| 01.00 | 01.30 | Circulated bottoms up |  | 12ºN340W | ° at | 2093 | m |  | AMC Pac R |  |
| 01.30 | 08.00 | Tripped out for Bit change layed out 1 stabiliser |  | 18.5 | ° at | 2235 | m |  | Lakes Pac R |  |
| 08.00 | 11.30 | Tripped in hole with Bit # 6 to 1183m |  | N340W | ° at |  | m |  | Xan Bore | 1 |
| 11.30 | 12.00 | Filled pipe broke circulation |  |  | ° at |  | m |  | Bayrtes | 27 |
| 12.00 | 13.30 | Slipped blockline |  |  | ° at |  | m |  | Potassium Chloride | 84 |
| 13.30 | 14.30 | Tripped in hole to 1738m resistance at 1720m 10k |  |  | ° at |  | m |  |  |  |
| 14.30 | 15.00 | Filled pipe |  |  |  |  |
| 15.00 | 17.00 | Tripped in hole to 2390m |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
| 17.00 | 17.30 | Picked up Kelly washed to bottom at 2403m |  | Liner | 140 | mm |  | Liner | 140 | mm |
| 17.30 | 24.00 | Drilled 156mm hole from 2403m to 2413m |  | Pressure | 10,600 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP | 223 | f/min |  | A.V. DP |  | Ft/min |
|  |  | Tried various drilling parameters to try and increase |  | A.V. DC | 394 | f/min |  | A.V. DC |  | Ft//mn |
|  |  | the drilling rate |  | SPM | 40 |  | SPM |  |
|  |  |  |  | GPM | 240 |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 7" | inch |
|  |  | Hunt 17 Camp 4 |  | Class Bulk |  |  | Weight | 26 | ppf |
|  |  | Lakes 4 |  | % |  |  |  | Grade | K-55 |  |
|  |  | Mud logger 2 |  | % |  |  |  | Connection | BTC |  |
|  |  | Farley Riggs 4 |  | % |  |  |  | Joints | 117 |  |
|  |  | RMN 1 |  | % |  |  |  | Length | RT-Brd Hd 5.0 | m |
| Days since | LTA |  |  | Av. Wt |  |  | Shoe | 1376m from RKB | m |

,66